SEW-EURODRIVE SA supplies some of its largest drives ever to a Canadian mine

20 April 2017: A 24 t ZDN hoist drive, representing one of the largest single units from SEW-EURODRIVE South Africa to date, is to be supplied to a mine in Canada for a hoisting application. Traditionally known as specialising in smaller geared motors for conveyor applications, the project highlights the OEM’s capability to manufacture custom components up to the size and complexity of girth gears.

The order for the fast-track project was received in December 2016, with the initial kick-off meeting held in January 2017, Rudi Swanepoel, Head of Projects, states. “To the best of my knowledge, this is the biggest unit that SEW-EURODRIVE South Africa has ever supplied. In my experience, I have never quoted on a unit of this magnitude before. It is a real feather in our caps, especially seeing we were awarded the project by a leading competitor, which gives us a good foot in the door in securing future orders.”

The global presence of SEW-EURODRIVE is another major factor in securing this flagship project, with the ZDN 3 HSN 1670 hoist drive being designed and manufactured in the Czech Republic. The unit has a 35-week lead time, due to the fact that every single component has to be custom-machined due to its size. This is a reasonable timeframe, given that the gross weight of the unit is just on 24 t.

The hoist drive has two input shafts, driven by two 1 000 kW motors, driving helical bevel gears that, in turn, drive the single output shaft of the gearbox, and thereby the specific hoisting application. “The reason we had to do this was in order to comply with the specific requirements of the customer, who is looking to standardise on 1 000 kW units on-site. This means a more streamlined and cost-effective stockholding for all applications.”

The hoist drive features special oil coolers fitted for thermal and heat dissipation, including additional auxiliary equipment. Heat dissipation is a critical consideration, because the higher the kilowatt rating, the higher the required thermal rating of the gearbox will be, which calls for additional cooling.

The huge amount of torque generated on the output shaft is an astonishing ± 1.5 million Nm, as opposed to 475 000 Nm for the largest X-Series industrial gear unit produced by SEW-EURODRIVE to date. Due to the high torque requirements, the OEM was also able to assist with special tangential keys on the output shaft. “The application of the hoist drive is to convey both mineworkers and goods, which meant that strict health and safety requirements and safety factors had to be accommodated,” Swanepoel highlights. This also meant that a much higher service factor had to be taken into consideration.

SEW-EURODRIVE South Africa subsequently clinched a major order for the second stage of the project, a ML Series unit for a goods-only application, which is currently being assembled at the OEM’s manufacturing facility in China to international DIN standards. The power rating of this second hoist drive is 1 000 kW, with a nominal torque of 293 000 kNm.

“The second unit is going to the same mine, but the application is a goods-only hoist lift in a deeper underground section for ore transportation. This is also a one-off order, with special attention paid to the service factor and maintainability in order to increase its cost-effectiveness,” Swanepoel explains. The second unit, clocking in at about 11 t, will have a 24-week delivery period.

SEW-EURODRIVE South Africa is executing the project in conjunction with its main client. “We have the global capability to supply and service such major projects. Combined with our competitive pricing, we can also become involved at the design stage by assisting the customer with calculations and drawings,” Swanepoel concludes.

Ends

Connect with SEW-EURODRIVE on Facebook to receive the company’s latest news:

www.facebook.com/SEWEurodriveSA

Media Contact
Nomvelo Buthelezi
NGAGE Public Relations 
Phone: (011) 867-7763

Fax: 086 512 3352
Cell: 083 408 8911
Email: nomvelo@ngage.co.za
Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za